## Slide 1
Recovery-Aware Execution Agent
for Hierarchical Scientific Agents
Executor + Recovery Layer for Physical Labs
Sissi Feng
Alan Group

## Slide 2
Motivation: Why Recovery is the Bottleneck
PHYSICAL LAB REALITY
Devices fail unexpectedly
Communication interrupts
Control systems drift
Irreversible actions exist
Planning agents fail at the boundary between reasoning and physical execution.

## Slide 3
Position in El Agente Q Architecture
Planner
Hierarchical Agents
Executor + Recovery
YOU ARE HERE
Physical World

## Slide 4
What Existing Systems Miss
Current Agent Recovery
Retry the same action
Change parameters randomly
Switch to different tool
Missing Physical Semantics
Irreversibility - actions cannot be undone
Sample Status - material may be compromised
Safety Envelope - physical limits exist
Tool calling is not execution semantics. Retry is not recovery.

## Slide 5
Core Design Principles
1
Deterministic Safety First
Safety checks are hardcoded, not learned. No LLM in the safety loop.
2
Recovery Decoupled from Workflow
Recovery logic is independent of experiment structure.
3
Explicit Execution Semantics
Contracts, preconditions, postconditions are first-class.
4
Scientific Anomaly =/= Error
Unexpected results may be discoveries, not failures.
Principles derived from FSD and industrial control systems

## Slide 6
System Overview: Execution Layer Architecture
Plan Input
Supervisor
GuardedExecutor
PostCheck
ErrorClassifier
Signature + Policy
Key Components
Supervisor - Orchestrates execution loop
GuardedExecutor - Pre/post condition checks
PostCheck - Verifies action outcomes
ErrorClassifier - Maps errors to profiles
Signature - Fault pattern detection
Policy - Recovery decision engine
Runtime execution system, not an LLM agent.

## Slide 7
From Hardcoded Rules to Policy-Driven Recovery
Before: Scattered If-Else
if error == "overshoot":
cool_down()
retry()
elif error == "timeout":
wait(2)
retry()
elif error == "sensor_fail":
abort()
elif temp > 130:
emergency_stop()
...
->
After: Policy Engine
profile = classify(error)
signature = analyze(history)
decision = policy(
error_type,
signature_mode,
stage,
retry_count
)
execute(decision.actions)

## Slide 8
Error -> Signature -> Policy Pipeline
HardwareError
Raw error
->
ErrorProfile
unsafe / recoverable
->
Signature
drift / oscillation / stall
->
Decision
retry / degrade / abort
DRIFT
Steady increase
OSCILLATION
Swings up/down
STALL
No change
NOISY
High variance
Recovery is not if-else. It is three-layer semantic compression.

## Slide 9
Scientific Anomaly Channel
Critical for Continuous Discovery
ANOMALY DETECTED
Safety Anomaly
ABORT
Protect equipment
Execution Anomaly
RECOVER
Retry or degrade
Scientific Anomaly
PRESERVE
Anomalous but valid
Discovery happens in the offline analysis channel, not in recovery logic.
This implements "critical state for continuous discovery" from Alan's second paper.

## Slide 10
Safety and Irreversibility Guarantees
CORE GUARANTEES
1
Unsafe Preemption
Safety violations trigger immediate cool_down before any other action
2
Irreversible Action Tracking
Sample status tracked: intact / compromised / destroyed
3
Terminal Invariants on Abort
Shutdown verifies safe state: heating == False, status == idle
Examples
temp > 130C
Immediate cool_down, then degrade or abort
electrochem_started
Sample marked compromised, cannot revert
Any agent built on this layer will not cause equipment damage.

## Slide 11
Interface to Hierarchical Agents
1
execute_plan(plan) -> RunResult
Main entry point. Takes a plan from upper agent, returns execution outcome.
2
RecoveryAdvisor hook
Optional callback for upper agent to provide recovery hints.
3
RunObserver / event stream
Real-time event stream for monitoring: telemetry, decisions, errors.
Design Philosophy
I do not touch planning
I only provide reliable execution backend
Alan agents only need these three interfaces

## Slide 12
Example: Heater Overshoot Case
0s
Goal: Heat to 120C
5s
Monitoring... current 60C
10s
Monitoring... current 100C
12s
OVERSHOOT: 128C, exceeds target
12s
Signature: drift | Decision: DEGRADE
13s
Execute: cool_down()
14s
Execute: set_temperature(110)
15s
Stabilized at 110C, continue
Recovery Analysis
TARGET
120C
OVERSHOOT TO
128C (still safe)
SIGNATURE
drift
DECISION
DEGRADE to 110C
SAMPLE
compromised
Not retry. Not abort. Semantic recovery.

## Slide 13
Metrics and Verifiability
recovery_steps
Number of actions to recover from each error type
time_to_recover
Time from error detection to stable state
abort_rate
Percentage of runs requiring full abort
safety_violations
Count of safety envelope breaches
anomalous_preserved
Scientific anomalies captured for analysis
sample_status_dist
Distribution: intact / compromised / destroyed
This is an engineering system. Not "looks intelligent" - measurably reliable.

## Slide 14
Roadmap: Integration with Alan Agents
1
Policy-Driven Recovery
Deterministic recovery engine with signature analysis and configurable policies
NOW
2
RecoveryAdvisor via LLM
Connect to Alan reasoning agent for complex recovery decisions
NEXT
3
Self-Organizing Graph
Execution graph learns and adapts from experience
FUTURE

## Slide 15
1
Hierarchical agents need a physically grounded execution layer
2
Recovery is the foundation of continuous discovery
3
This layer makes Alan's architecture deployable in real labs
Infrastructure-level contribution, not a single agent idea